## Slide 1: A Coherent and Managed Runtime for ML on the SCC
KC Sivaramakrishnan Lukasz Ziarek Suresh Jagannathan
Purdue University SUNY Buffalo Purdue University

## Slide 2: Big Picture
No cache coherence
Message passing buffers
Distributed programming
RCCE, MPI, TCP/IP
Intel SCC
Cluster of Machines
Shared memory
Software Managed Cache-Coherence (SMC)
Cache Coherent
No change to programming model
Automatic memory management
??
Can we program SCC as a cache coherent machine?

## Slide 3: Intel SCC Architecture
Private Memory
Core 0
Private Memory
Core 47
Private Memory
Core 2
Private Memory
Core 1
...
Shared Memory
(off chip)
No Cache-Coherence
(Caching disabled)
Software Managed Cache
(Release Consistency)
Message Passing Buffers
(On die, 8KB per core)
How to provide an efficient cache coherence layer?

## Slide 4: SMP Programming Model for SCC
Abstraction Layer
Program
Desirable properties
  Single address space
  Cache coherence
  Sequential consistency
  Automatic memory management
  Utilize MPB for inter-core communication
Abstraction Layer – MultiMLton VM
  A new GC to provide coherent and managed global address space
  Mapping first-class channel communication on to the MPB
SCC

## Slide 5: Programming Model
MultiMLton
  Safety, scalability, ready for future manycore processors
  Parallel extension of MLton – a whole-program, optimizing Standard ML compiler
  Immutability is default, mutations are explicit
ACML – first-class message passing language
C
send (c, v)
v  recv (c)
Automatic memory management
Notes: * sharing mutable objects

## Slide 6: Coherent and Managed Address Space
Notes: * Slide 2 -- Summary – Problem of too many -- How can efficient program these resources?
Slide 5,6 -- Automatic memory management. Think about combining the slides. Titles.
* Slide 17,18 -- Summary -- sender blocks, value is local, receiver appears, message is transferred over the MPB.
* Slide 19 -- Rename the lines

## Slide 7: Coherent and Managed Address Space
Requirements
  Single global address space
  Memory consistency
  Independent core-local GC
Thread-local GC!
Private-nursery GC
Local heap GC
On-the-fly GC
Thread-specific heap GC

## Slide 8: Thread-local GC for SCC
Core 0
Core 0
Core 0
Local Heap
Private
Memory
Local Heap
Private
Memory
Local Heap
Private
Memory
…
Shared Memory
Uncached Shared Heap
(Mutable Objects)
Cached Shared Heap
(Immutable Objects)
Consistency preservation
  No inter-coherence-domain pointers!
Independent collection of local heaps
Caching disabled
SMC - Caching enabled
Notes: * Emphasize that local heap can be collected locally, and there are no inter-coherence domain pointers.

## Slide 9: Heap Invariant Preservation
Uncached Shared Heap
Cached Shared Heap
Local Heap
rm
xm
yim
Uncached Shared Heap
Cached Shared Heap
Local Heap
rm
xm
yim
r := x
FWD
FWD
Mutator needs Read Barriers!
Write barrier -- Globalization

## Slide 10: Maintaining Consistency
Local heap objects are not shared by definition
Uncached shared heap is consistent by construction
Cached shared heap (CSH) uses SMC
  Invalidation and flush has to be managed by the runtime
  Unwise to invalidate before every CSH read and flush after every CSH write
Solution
  Key observation: CSH only stores immutable objects!

## Slide 11: Ensuring Consistency (Reads)
Uncached Shared Heap
Cached Shared Heap
MAX_CSH_ADDR
X
0: read(x)
Uncached Shared Heap
Cached Shared Heap
MAX_CSH_ADDR == X
Invalidate before read – smcAcquire()
  Maintain MAX_CSH_ADDR at each core
Assume values at ADDR < MAX_CSH_ADDR are up-to-date
Up-to-date
Stale
Up-to-date
Stale
  Cache invalidation combined with read barrier

## Slide 12: Ensuring Consistency (Reads)
No need to invalidate before read (y) where
y < MAX_CSH_ADDR
Why?
  Bump pointer allocation
  All objects in CSH are immutable
  y < MAX_CSH_ADDR  Cache invalidated after y was created
Notes: (1)Heap grows from left to right
(2) Recall that the objects in CSH are immutable objects. The value of immutable objects, by definition, will not change after allocation.
Since MAX_CSH_ADDR is > y, it must be the case that we have read a CSH address which is greater than order equal to y. Hence, we would have performed an invalidation after the object y was allocated. Hence, there is no need to perform invalidation during read of y.

## Slide 13: Ensuring Consistency (Writes)
Writes to shared heap occurs only during globalization
Flush cache after globalization
  smcRelease()
Cache flush combined with write barrier

## Slide 14: Garbage Collection
Local heaps are collected independently!
Shared heaps are collected after stopping all of the cores
  Proceeds in SPMD fashion
  Each core prepares the shared heap reachable set independently
  One core collects the shared heap
Sansom’s dual mode GC
  A good fit for SCC!

## Slide 15: GC Evaluation
8 MultiMLton benchmarks
Memory Access profile
  89% local heap, 10% cached shared heap, 1% uncached shared heap
  Almost all accesses are cacheable!
48% faster
Notes: * At 48 cores, 48% faster than using a single shared heap.

## Slide 16: ACML Channels on MPB
Notes: * Slide 2 -- Summary – Problem of too many -- How can efficient program these resources?
Slide 5,6 -- Automatic memory management. Think about combining the slides. Titles.
* Slide 17,18 -- Summary -- sender blocks, value is local, receiver appears, message is transferred over the MPB.
* Slide 19 -- Rename the lines

## Slide 17: ACML Channels on MPB
Challenges
  First-class objects
  Multiple senders/receivers can share the same channel
  Unbounded
  Synchronous and asynchronous
A blocked communication does not block core
Channel Implementation
datatype ‘a chan = {sendQ : (‘a * unit thread) Q.t,
recvQ : (‘a thread) Q.t}

## Slide 18: Specializing Channel Communication
Message mutability
  Mutable messages must be globalized
    Must maintain consistency
  Immutable messages can utilize MPB
Notes: Explain all of the cases from the sender’s perspective. The receiver case will be the dual of this.
Case 1 is straight-forward, and requires no special handling

## Slide 19: Sender Blocks
Channel in shared heap, message is immutable and in local heap
Shared Heap
Local Heap
C
t1
Vim
t1:send(c,v)
Local Heap
t2
Shared Heap
Local Heap
C
t1
Vim
Local Heap
t2
Core 0
Core 1
Core 1
Core 0

## Slide 20: Receiver Interrupts
t2: recv(c)
Shared Heap
Local Heap
C
t1
Vim
Local Heap
t2
Core 1 interrupts core 0 to initiate transfer over MPB
Core 0
Core 1
Shared Heap
Local Heap
t1
Vim
Local Heap
t2
Core 0
Core 1
Vim
C

## Slide 21: Message Passing Evaluation
On 48-cores, MPB only 9% faster
Inter-core interrupt are expensive
  Context switches + idling cores + small messages
  Polling is not an option due to user-level threading
SHM
MPB

## Slide 22: Conclusion
Cache coherent runtime for ML on SCC
  Thread-local GC
    Single address space, Cache coherence, Concurrent collections
    Most memory accesses are cacheable
  Channel communication over MPB
    Inter-core interrupts are expensive

## Slide 23: Questions?
http://multimlton.cs.purdue.edu

## Slide 24: Read Barrier
pointer readBarrier (pointer p) {
if (getHeader (p) == FORWARDED) {
//A globalized object
p = *(pointer*)p;
if (p > MAX_CSH_ADDR) {
smcAcquire ();
MAX_CSH_ADDR = p;
}
}
return p;
}

## Slide 25: Write Barrier
val writeBarrier (Ref r, Val v) {
if (isObjptr (v) && isInSharedHeap (r) &&
isInLocalHeap (v)) { v = globalize (v);
smcRelease ();
}
return v;
}

## Slide 26: Case 4
Channel in shared heap, message is mutable and in local heap
Shared Heap
Local Heap
C
t1
Vm
t1:send(c,v)
Shared Heap
Local Heap
C
t1
Vm
Globalize the mutable message

## Slide 27: Case 2
Channel in Shared heap, Primitive-valued message
Shared Heap
Local Heap
C
t1
t1:send(c,0)
Shared Heap
Local Heap
C
t1
Remembered
Set

## Slide 28: Case 3 – Sender Blocks
Channel in shared heap, message in shared heap
Shared Heap
Local Heap
C
t1
V
t1:send(c,v)
Local Heap
t2
Shared Heap
Local Heap
C
t1
V
Local Heap
t2
Remembered
Set
Core 0
Core 1
Core 1

## Slide 29: Case 3 – Receiver Unblocks
t2:recv(c)
Shared Heap
Local Heap
C
t1
V
Local Heap
t2
Core 1
Core 0
Shared Heap
Local Heap
C
t1
V
Local Heap
t2
Core 1
Core 0